## Slide 1
GPR-based Model Reconstruction System for Underground Utilities Using GPRNet
Jinglun Feng
Robotics Lab, City College of New York

## Slide 2
GPR Introduction
What is GPR?
Ground Penetration Radar
Why GPR?
None-Destructively Testing (NDT)
How it works?
EM Wave, Two-way travel time
Notes: The GPR method is a wave propagation technique that transmits a pulse of polarized high-frequency radar waves into the subsurface media. EM wave attenuates as it travels in media and reflects when it encounters a material change. GPR antenna would thus record the strength and traveled time of each reflected pulse.

## Slide 3
GPR Preliminary and Challenges
A-Scan Raw Data
Consecutive Scan
B-Scan Raw Data
Direct
Coupling
B-Scan Hyperbola
    GPR Background Noise Data
    Unknow Subsurface Dielectric
    Inefficient and Tideious GPR Data Collection
    Hard Interpretation and Abstract Visualization
GPR Migration: The mathematical-based technique which serves as the traditional GPR imaging tools, enabling to convert the unfocused raw B-scan radargram data into a focused target
GPR Background Noise
？
Notes: GPR works by sending a pulse of polarized high-frequency electromagnetic (EM) wave into the subsurface media. EM wave attenuates as it travels in media and reflects when it encounters a material change. GPR antenna would thus record the strength and traveled time of each reflected pulse. The received signal is called an \emph{A-scan}. When GPR antenna surveys over a subsurface object, it produces a series of A-scans at different positions, and the ensemble of A-scans forms a \emph{B-scan}. The B-scan contains the hyperbolic feature which would indicate the location of the target.

## Slide 4
    GPR Background Noise Data
    Unknow Subsurface Dielectric
    Manually GPR Data Collection
    Hard Interpretation and Abstract Visualization
    Remove GPR Background Noise Data
    Estimate Unknow Subsurface Dielectric
    Automatic GPR Data Collection
    Intuitive Interpretation and Fridenly Visualization
Motivations
Automatic GPR Inspection
Goal:
A robot which can automatic collect GPR data and reconstruct 3D model of underground cylinder objects

## Slide 5
Omni-GPR-Cart Platform
Motion Model:
Intel NUC
Battery
RealSense Camera
GSSI GPR

## Slide 6
Conventional GPR Imaging Algorithm
Back Projection
: the -th A-scan measurement in -th B-scan data
: the -th B-scan consisting of A-scans
amplitude of A-scan signal
: traveling time
the total samples in a A-scan measurement
A-Scan Raw Data

## Slide 7
Conventional GPR Imaging Algorithm
“The brighter the intersection, the more possible an object exists”

## Slide 8
MigrationNet Architecture
256 channels input data, and further down-sampling into 128 and 64 channels in spatial domain.
Multiple Spatial Resolution Encoder (MSRE)
up-sampling group
each group contains two convolutional layers and one deconvolutional layer
⊕ represents the skip connection while ①-⑨ indicate each last encoder layer
Model Design
Inspired by [1]
[1] Lin, Tsung-Yi, et al. "Feature pyramid networks for object detection." Proceedings of the IEEE conference on computer vision and pattern recognition. 2017.

## Slide 9
Loss Design
Loss Design
Inspired by [2]
Loss Performance Comparison
[2] Zhou Wang, Alan C Bovik, Hamid R Sheikh, and Eero P Si-moncelli. Image quality assessment: from error visibility to structural similarity. IEEE transactions on image processing,13(4):600–612, 2004.
Similarity matters!!
are standard deviations as an estimation of image contrast respectively.
is the predicted image while is the ground truth image.

## Slide 10
3D Subsurface Modelling -- Motivation
MigrationNet
Challenge: A 2D reconstruction is not able to reveal the subsurface targets
We need to obtain 3D underground objects reconstruction
？

## Slide 11
 | Synthetic Data | Field Data
Test Models | 137 | 1
GPR B-scan Data | 1507 | 1 * 120
Point Cloud Data | 685 | 12
We use gprMax [3] create a new dataset which contains both
synthetic and field GPR / point cloud data
Data Setup and 3D Registration
Input
Ground
Truth
We use MigrationNet to firstly obtain the 2D cross-section images, then register them into the 3D domain
[3] Warren, Craig, Antonios Giannopoulos, and Iraklis Giannakis. "gprMax: Open source software to simulate electromagnetic wave propagation for Ground Penetrating Radar." Computer Physics Communications 209 (2016): 163-170.

## Slide 12
GPRNet Architecture
Encoder Strength [4]: could extract multiple resolution information of the input data, which leads a better performance on small structure completion.
Decoder Strength [5]: 1) good at predicting the global geometry of point cloud; 2) good at generating a smooth local feature
[5] Z. Huang, Y. Yu, J. Xu, F. Ni, and X. Le, “Pf-net: Point fractal network for 3d point cloud completion,” in Proceedings of the IEEE/CVF Conference on Computer Vision and Pattern Recognition, 2020, pp.7662–7670
[4] W. Yuan, T. Khot, D. Held, C. Mertz, and M. Hebert, “Pcn: Point completion network,” in2018 International Conference on 3D Vision(3DV). IEEE, 2018, pp. 728–737.

## Slide 13
Subsurface Modelling Results – Synthetic Data

## Slide 14
Subsurface Modelling Results – Field Data

## Slide 15
Other Subsurface Modelling Results

## Slide 16
&
Questions